## Slide 1: Architectural Test SIG Call –Minutes
Thur, 27Apr2023 8am Pacific  Daylight  Time
See slide 7 for agenda

## Slide 2
RISC-V International meetings involve participation by industry competitors, and it is the intention of RISC-V International to conduct all its activities in accordance with applicable antitrust and competition laws. It is therefore extremely important that attendees adhere to meeting agendas, and be aware of, and not participate in, any activities that are prohibited under applicable US state, federal or foreign antitrust and competition laws.
Examples of types of actions that are prohibited at RISC-V International meetings and in connection with RISC-V International activities are described in the RISC-V International Regulations Article 7 available here: https://riscv.org/regulations/
If you have questions about these matters, please contact your company counsel.
Antitrust Policy Notice

## Slide 3
RISC-V is a free and open ISA enabling a new era of processor innovation through open standard collaboration. Born in academia and research, RISC-V ISA delivers a new level of free, extensible software and hardware freedom on architecture, paving the way for the next 50 years of computing design and innovation.
We are a transparent, collaborative community where all are welcomed, and all members are encouraged to participate. We are a continuous improvement organization. If you see something that can be improved, please tell us. help@riscv.org
We as members, contributors, and leaders pledge to make participation in our community a harassment-free experience for everyone.
https://riscv.org/community/community-code-of-conduct/
Collaborative & Welcoming Community

## Slide 4: Only RISC-V Members May Attend
Non-members are asked to please leave.
Members share IP protection by virtue of their common membership agreement. Non-members being present jeopardizes that protection
It is easy to become a member. Check out riscv.org/membership
If you need work done between non-members or or other orgs and RISC-V, please use a joint working group (JWG).
  used to allow non-members in SIGs but the SIGs purpose has changed.
Please put your name and company (in parens after your name) as your zoom name. If you are an individual member just use the word “individual” instead of company name.
Non-member guests may present to the group but should only stay for the presentation. Guests should leave for any follow on discussions.
RISC-V attendance

## Slide 5: SIG Charter
The Architectural Compatibility Test SIG is an umbrella group that will provide guidance, strategy and oversight for the development of tests used to help find incompatibilities with the RISC-V Architecture as a step in the Architectural Compatibility self-certification process
The group will:
Guide Development of:
  Architectural tests for RISC-V implementations covering ratified and in-flight specifications for
    Architectural versions, standard extensions, and implementation options.
  Tools and infrastructure to help identify architectural incompatibilities in implementations
Work with TSC and Chairs for resources to get the above work done.
Mentor or arrange for mentoring for the resources to get the above work done

## Slide 6: Adminstrative Pointers
Chair – James Shi shiqinghao.sqh@alibaba-inc.com Co-chair – Neel Gala neel.gala@incoresemi.com
SIG Email sig-arch-test@lists.riscv.org. Notetakers: please send emails to allen.baum@esperantotech.com
Meetings -Bi-monthly at 8am Pacific time on 2nd/4th Thursdays.
Documents, calendar, roster, etc. in
  https://sites.google.com/a/riscv.org/risc-v-staff/home/tech-groups-cal
  https://drive.google.com/drive/folders/1C70-DJPSV2HxNPbHg6qL9wvVadlmAB2h ACT test: dev docs / coverage reports / released reports
  https://drive.google.com/drive/folders/1DemKMAD3D0Ka1MeESRoVCJipSrwiUlEs lifecycle in ”policies/supporting docs” folder, gaps in “planning” folder, arch-test specific in “information->content->arch-test”)
Git repositories docs riscv  tools
  https://github.com/ riscv-non-isa /riscv-arch-test/tree/master/doc tests https://github.com/riscv-non-isa/riscv-arch-test
  https://github.com/riscv-software-src/riscof/tree/master/docs riscof https://github.com/riscv-software-src /riscof
  https://github.com/riscv-software-src/riscv-ctg/tree/master/docs Test Gen. https://github.com/riscv-software-src /riscv-ctg
  https://github.com/riscv-software-src/riscv-isac/tree/master/docs YAML, WARL config https://github.com/riscv-software-src /riscv-config/
  https://github.com/riscv/sail-riscv/tree/master/doc Sail formal model https://github.com/riscv/sail-riscv/
  https://github.com/riscv-admin/architecture-test minutes, charter
  https://github.com/InspireSemi/riscof_install_example_DUT sail install helper
JIRA: https://jira.riscv.org/projects/CSC/issues/CSC-1?filter=allopenissues
Dev Partner work: https://github.com/orgs/riscv-admin/projects/2/views/4
Sail annotated ISA spec: in https://github.com/rems-project/riscv-isa-manual/blob/sail/
  README.SAIL how to annotate annotated unpriv spec release/riscv-spec-sail-draft.pdf
  release/riscv-spec-sail-draft.pdf  annotated source annotated priv spec release/riscv-privileged-sail-draft.pdf
  https://us02web.zoom.us/rec/share/-XIYazzhIBbQoiZdarCfebdjxjDWiVhf-LxnuVrliN4Bc30yf17ztKkKDU4Og54b.fArPPqnuR-NiXpQU
  Tutorial Passcode: tHAR#5$V

## Slide 7: Meeting Agenda
Updates, Status, Progress:
  (non)election – Introduction to new chair
  Euro RV Summit Barcelona 05-09 June
Next steps and Ongoing maintenance
  Open PR/issue review
  Future priorities (see slide 11)
  Making Jenkins tests be more C/I friendly

## Slide 8: Discussion
Open issues on riscv-arch-test repo Issue #339: Problem w/nested ifndef inside #defined macro RVTEST_INIT_GPRS in arch_test.h - Prev Chair – Problem with using a C style macro. Fix by converting to an assembly macro.. Issue #338 : LI macro throwing shift count out of range warnings for RV64 - Prev Chair - Aware of the issue and the fix ill be pushed in soon. No actual bug in the code it works as intended i.e the warnings can be ignored
Issue #337: Incorrect macro for register save in arch_test.h - Prev Chair - Need to rename SIGUPD to RVTEST_SIGUPD. Fixed in next version Issue #336: Warning messages about missing macro code in arch_test.h - Seagate - Insuffiicient info regarding the functionality defined by these macros and missing instructions on how to define them. Needs update to documentation Prev Chair – Documentation Is currently being rewritten. Note that these will return to the instruction that was interrupted, so can’t be executed inside an infinite loop without a way to escape. <AI: document a standard way to escape, e.g. seeing if mtrap_sigptr has changed> - Incore - Would be a good idea to include which registers may be clobbered inside these routines after returning to the test, and what their values will be Prev Chair – Documentation Is currently being rewritten coming Issue #335: Untestable instructions/functionality should be documented - Seagate - documentation needed for kinds of tests we never expect/aren't planning to write in the near future, e.g. such as memory model, WFI Prev Chair - WFI can be tested right now using mtime-mtimecmp. - Inspire – WFI has multiple legal behaviors for including Noop, interrupt taken/not taken based on global interrupts or take illegal instruction trap based on TW. Prev Chair – Great example. AI: <prev chair> write a new SoW for WFI tests
Public Service Announcement The latest sail model is incompatible with the older version. It needs sail v0.15 to compile which is only available on opam v4.08+. To update the RISCV SAIL model, you will need to update environment and recompile from scratch
Can memory litmus tests be used for ACT? see - https://github.com/litmus-tests/litmus-tests-riscv​ -Test time is too high: short routines are run concurrently on 2 or more harts​ for large # of passes. Would be ok for SAIL sim time but might not be acceptable for RTL - Can’t guarantee specific ordering/scenario takes place by concurrently testing them Q: How can we generate signatures for such tests? A: Can be potentially self checking A: If #of legal outcomes is a small &deterministic, RISCOF can test for at least one match in these cases - SAIL model support Q: Can we use sail model to run these tests? Q: How to introduce non-determinism for such cases A: Might be better to trigger non-determinism through an external event generator rather than micro-architectural timing differences due to non-deterministic paths (e.gcaches etc). A: Should explore testing minimally or introducing external control to ensure that total run time per test can be kept small. Don’t want to cross into DV territory AI: RISCV- Will explore litmus tests, try to get sail model support answers and test timings.
Chat comments:
RV: Should we look at Linux Test Project for memory model tests Chair: Requires (multi-core) Linux Kernel boot, so more of proof of concept Prev_Chair: we should look at what they do and see if we can adapt it to our test methodology

## Slide 9: Decisions & Action Items
Decisions ()
No self-checking tests unless absolutely necessary (e.g. for non-deterministic tests)
Add new mailing list for branding questions
Need a tool to - expand profile name to riscv-config format, or - provide a pre-populated YAML doc with minimum requirements
Need a tool that checks whether one riscv-config YAML file is the superset of another
Outstanding Action Items
Add test failure debug hints in readme <inspire, incore, axiomise>
Look for and setup ref-signature-as a service site using docker image of Sail and tests < Chair > funding for this yes
Develop plugins for podman as well as remote container < HC? >
Propose new wording for Bare mode encoding restrictions <chair>
Set up a TG to define Async Event Generator specs (test interface, Model interface, generator SW that can interface to RTL and simulators, sample shims for Spike and Sail <chair>
(issue #203) Add fence test with all set bits) <dev partners>
(issue#119) Add rm field fence.i walking ones test <chair/dev partners>
Rewrite test-Format_spec, splitting into test dev guidelines and model reqs, update >
Add PTE<level> to Sail trace as an option <Sail>
Add TLB disable option to Sail<Sail>
Add F/D status.FS tests<chair/dev partners>
decide how to test for profile specified arch options
Generate list of testable profile item
Determine who is responsible profile definition? (TSC / Krste / Greg):
Define github file that describes existing tests, to be updated on every merge.
explore litmus tests, try to get sail model support answers and test timings < RISCV>
document a std way to escape an interrupt wait loop in tests, <prev chair>
write a new SoW for WFI tests <prev chair>
Write a new SoW for uncompressed, unaligned instruction traps when C-ext is enabled <prev chair>

## Slide 10: BACKUP

## Slide 11: Future Topics
Split and update Test_Format_Spec into
  TestDev_Guideline_Spec – primarily the structure of tests & required/optional RVTEST_ macros
  ACT_interface_Spec – primarily all the RVMODEL_ macros
Close outstanding issues & pull requests
Limiting test size (size of code, data, signature area?)
Reference Signature as a Service (Golden Model WG) and Docker/Podman containers
Support for handling constrained non deterministic results (e.g. misaligned load/store/branch)
Trick boxes of timing/concurrency support
  Interrupt event generator ( interrupt testing)
  Memory event generator (LR/SC, Atomic ops, WRS, mem model (TSO, WMO)
  Debug/Trace command interface (Etrace, Ntrace) 
Minimal TLB / cache op test support (likely requires simple cache/TLB models w/ controlled enough behavior to test) .
DUT debug support: out-of-line assertion macro, FP and Vector assertions (CSR assertions?)
  (currently very model specific, and costly because all inlined code define an API subroutine call with a standard narrow interface).
OS support? (besides Debian, Ubuntu): e.g. Centos, Suse? RockyLinux, Windows, Mac, etc.
Tools: more concise coverage syntax, riscv-config YAML GUI generation, riscv-config YAML subset comparison
Decisions: allow dynamically generated tests (e.g. vector configs), machine generated SAIL for CSR R/W legalization?
Making Jenkins tests be more C/I friendly

## Slide 12: Trap Handler VM translation
M-mode
PA mapping
Trampoline Save
Reg Save
VMtst_Begin/End
Code Begin/End
Data Begin/End
Sig Begin/End
M-mode
Trampoline Save
Reg Save
VMtst_Begin/End
Code Begin/End
Data Begin/End
Sig Begin/End
S/U-mode
Trampoline Save
Reg Save
VMtst_Begin/End
Code Begin/End
Data Begin/End
Sig Begin/End
HS/US -mode
VSscratch
Sscratch
Mscratch
Code
Segment
Data
Segment
Sig
Segment
VMTst
Segment
S,U-mode
VM mapping
Code
Segment
VS/VU-mode
Guest mapping
Sig
Segment
VMTst
Segment
VMTst
Segment
Data
Segment
VMTst
Segment
Code
Segment
Sig
Segment
VMTst
Segment
Data
Segment
VMTst
Segment
The trap handler initializes this data structure to point to Mmode mappings, and the scratch registers to point to the data structure.
A test that changes the mapping must change the 8 segment pointer pairs (and the associated mode’s scratch register if changing data segment mapping) to match the mapping offset.
Permission changes don’t need to update these pointers.
The VMTest segment can be assigned by the test to be an arbitrary VA that double maps a VA to a different aperture to the same segments with different permissions without affecting the trap handler
Fixed, known offsets

## Slide 13
FLD_RNG
FLD_RNG
FLD_RNG
Int64
rng_hi
Int64
rng_lo
union
List
CSR_STRUCT
union
struct
List()
native
CSR_STRUCT
CSR_STRUCT
CSR_STRUCT
Bitfld64
reset
int12
CSR_NUM
List
CSR_FMT
List
DEP_ELE
DEP_ELE
DEP_ELE
DEP_ELE
enum
dep_type
Bitfld6
fld_hi
int12
REG_NUM
Bitfld6
fld_lo
CSR_FMT
CSR_FMT
CSR_FMT
List
DEP_LIST
List
FLD_FMT
unchg, wr_val
near_up, near_dn,
nxt_up, nxt_dn,
large small,
extend, wpri, imm_val
CSR, Xreg, Freg, Vreg
Could be empty!
FLD_FMT
FLD_FMT
FLD_FMT
Bitfld6
fld_msb
List
FLD_RNG
Bitfld6
fld_lsb
fetch
check
When all DEP_ELEs are within FLD_RNGs, the FLD_FMT list describes the CSR field format
For each field in that format, search the FLD_COND list for a range that includes the wr_val, and apply the mapping function to update that field value)
Optional, unimplemented CSRs are encoded as bitmask with zero mask, zero value
FLD_ RNG
FLD_ RNG
FLD_RNG
Bitfld64 fld_msk
Bitfld64 fld_val
Notes:
For RV32, change bitfield64 to bitfield32
Int64 to Int32
int6 to int5
TBD: how to deal with shadow fields? Can shadow fields have dependencies? Need to point to shadowed field via
int12 csrnum, int6 fld_hi, int6 fld_lo.
Does WLRL need special handling?
If DEP_LIST is empty, then DEP_VAL must be empty
If FLD_FMT is empty, then the entire reg is RW (or RdOnly depending on CSR#) with no WARL fields
RdOnly is handled as rng_hi<rng_lo with map_func = unchg
FLD_ RNG
FLD_ RNG
FLD_ RNG
Int64?
rng_hi
Int64?
rng_lo
bitfield
Each list member describes a CSR field position, points to the list of legal value ranges for that field, and the mapping function for anything illegal.
Lists must be same leng &
In same order
Fld_hi==fld_lo
is a 1 bit field
containing a list of dependency values and the field format they describe
containing a list of legal value/ranges for that field
containing a list of each field in that format and its mapping function
A list of CSRs and a list of state each depend on to specify a format
LegalizeCSR(int12 CSR_num, Wr_data, mode)
enum
map_func
bitfield
imm_val
LGL_DEPS
LGL_DEPS
LGL_DEPS
List
FLD_RNG
Used to
dependency values
This defines which state are dependencies
This defines state values corresponding to a CSR format.
There can be multiple sets of dependency values for each format

## Slide 14: Draft Test_Dev Guidelines
Required Pre-Defined Macros – Macros that every test must include
RVTEST_CODE_BEGIN This saves state and conditionally initializes the trap handler and initializes gprs
RVTEST_CODE_END This conditionally saves the post-test GPR values, transitions to Mmode,
conditionally restores pre-test state and causes branches to test halt, then
conditionally installs the trap handler
RVTEST_DATA_BEGIN This initializes the a pointer to that trap signature area of the test signature,
and reserves space for a pointer to the save area used to save and restore state
modified by the trap handler .
RVTEST_DATA_END Contains the current trap signature pointer (if traps are enabled)
This macro marks the end of the test input data section with label rvtest_data_end
RVTEST_SIG_BEGIN Marks the beginning of the signature region with label rvtest_sig_begin and encapsulates
the RVMODEL_DATA_BEGIN macro . and label mtrap_sigptr
RVTEST_TSIG_BEGIN Marks the end of the signature pointer (if traps are enabled) and encapsulates the
the RVMODEL_DATA_END macro. and label rvtest_sig_end
RVTEST_SIG_END Contains the current trap signature pointer (if traps are enabled) ***FIXME-1/mode
This macro marks the end of the test input data section with label rvtest_data_end
RVTEST_CASE(CaseName, CondStr)
execute this case only if condition in cond_str are met
CaseName is arbitrary string
CondStr is evaluated to determine if the test-case is enabled and sets name variable
CondStr can also define compile time macros required for the test-case to be enabled.
The test-case must be delimited with an #ifdef CaseName/#endif pair
The format of CondStr can be found in https://riscof.readthedocs.io/en/latest/cond_spec.html#cond-spec
RVTEST_GOTO_MMODE This is used whenever a test halts to put it in Mode so it can restore all state*
RVTEST_GOTO_LOWER_MODE(mode) MRET to lower priv mode (requires identity mapped MMU if transitioning to a mode with different MMU state)
Helper Macros These are instantiated by the required macros
RVTEST_INIT_GPRS
RVTEST_TRAP_PROLOG sets up trap environment, depends on rvtest_strap_routine & rvtest_vtrap_routine
RVTEST_TRAP_HANDLER saves trap status in sig & rtn; depends on rvtest_strap_routine & rvtest_vtrap_routine
RVTEST_TRAP_EPILOG restores trap environment; depends on rvtest_strap_routine & rvtest_vtrap_routine
RVTEST_TRAP_SAVEAREA set up save area for trap; depends on rvtest_strap_routine & rvtest_vtrap_routine
RVTEST_SAVE_GPRS(tmpreg, saveaddr) saves all regs except tmpreg to saveaddr at test end if gpr_save defined
Required Pre-Defined Variables architecturally defined
SET_REL_TVAL_MSK (mask of which exceptions store data addrs in xtval.
(Defaults to 15, 13..12, 7..4, 3,1..0 , YAML can ovveride)) **update for H-ext
NUM_SPECD_INTCAUSES (defaults to 16, YAML can ovveride) ***fix for H-ext
NUM_SPECD_EXCPTCAUSES (defaults to 16, YAML can ovveride) ***fix for H-ext
Required predefined labels:
rvtest_entry_point The test must define this label to indicate the location to be used by the linker as the
entry point in the test. Generally, this would be before the RVMODEL_BOOT macro and
should belong to the text.init section.
gpr_save The test must define gpr_save after rvmodel_sig_end to mark where
registers get saved if rvtest_gpr_save is defined
rvtest_init
rvtest_[m,s,v]trap_routine used to conditionally instantiate helper macros, depending modes a test will trap into
Optional, Pre-defined Macros These are helper macros that make test generation easier. The include a set that gives a standard way of storing
signatures from the various registers, keeping track of the signature offset, offset overflow, and offset alignment
.
RVTEST_SIGBASE(BaseReg,Val) defines the base register used to update signature values
Register BaseReg is loaded with value Val, hidden_offset is initialized to zero
RVTEST_BASEUPD(BaseReg[oldBase[,newOff]]) [moves &] updates BaseReg past stored signature.
Hidden_offset is re-initialized to 0 afterwards
RVTEST_VALBASEUPD(BaseReg [, Offset])
RVTEST_SIGUPD( BaseReg, SigReg [, Offset])
RVTEST_SIGUPD_F( BaseReg, SigReg, FlagReg [, Offset])
RVTEST_SIGUPD_FID(BaseReg, SigReg, FlagReg [, Offset])
Updates the base reg by hidden or explicit offset. Flagreg is the gpr where fstatus CSR is loaded
**why is a flag register needed? The macro could copy fstatus into SigReg after storing it.
LI(rd,imm) must be used to load any constant whose value is not in -2048..2047 range
LA(rd, addr) must be used to load addresses that aren’t pre-loaded in memory
TBD Optional, Test-defined Variables
RVTEST_VA2PA perform a page table walk
RVTEST_GVA2PA perform a 2 level page table walk
rvtest_gpr_save enables saving registers at the end of the signature

## Slide 15: Draft: External Arch-Test Spec
Required, Model-defined Macros
These macros are be defined by the owner of the test target in the file model_test.h. These macros are required to define the signature regions and also the logic required to halt/exit the test.
RVMODEL_HALT
This macros must define the test-target halt mechanism. This macro is called when the test is to be terminated either due to completion or due to unsupported behavior. This macro could also include routines to dump the signature region to a file on the host system which can be used for comparison.
Optional Model Defined variables (**FIXME – need to complete)
RVMODEL_ADDR_SZ_ (default to the largest possible size if not defined)
RVMODEL_PHYS_ADDR_SZ (default to 57 for RV64, 34 for RV32S, 32 for RV32)
RVMODEL_CACHE_BLK_SZ (default to 64)
NUM_SPECED_INTCAUSES (default to 16) **FIXME for HEXT
NUM_SPECED_EXCPTCAUSES (default to 16) ) **FIXME for HEXT
RV_MODEL_FENCEI (default to fence.i)
RVTEST_DATA_REL_TVAL_MSK (bit-reversed mask of which exceptions store data addrs in xtval. Defaults to left aligned 0x0F05 (causes 4..7, 13, 15) **update for H-ext
RVTEST_DATA_REL_TVAL_MSK (bit-reversed mask of which exceptions store code addrs in xtval.
Defaults to left aligned 0xD008 (causes 0,1,3,12) **update for H-ext
GOTO_M_OP Defaults to csrr t4, CSR_MSTATUS. Change if illegal_op is delegated
RVTEST_E Defined by framework if model is RV32/64E
Model requirements:
Each xTVEC is either arbitrarily writable or initialized to a memory address that has RWX permissions and at least 580 bytes in size (specifically: (XLEN + 3* NUM_SPECD_INTCAUSES + 17) * 4). Altogether (up to 3) must not cross page boundaries
The hart exports a 4bit output signal which is the # of retired instructions during each cycle
The hart imports XLEN input interrupt signals
The hart can be configured to have as much memory as a test requires
The risv-config YAML for the core has all model defined variables and optional features implemented (**FIXME:list)
e.g. unaligned access, unaligned_partial_store, Zextensions implemented, opt_except_priorities, granularity, #PMPs, …
Optional, Model-defined Macros These are macros whose implementation must be defined by the DUT because they are platform specific. They include boot code, debug messaging routines, assertion checking, and eventually interfaces to asynch events like interrupts, concurrent memory accesses, and external debug.
RVMODEL_BOOT contains boot code for the test-target; may include emulation code or trap stub.
If the test-target enforces alignment or value restrictions on the mtvec csr, it is required that
this macro sets the value of mtvec to a region which is readable and writable by the M- mode.
***FIXME: must also specify stvec and vstevec and sizes (580 bytes)
The boot code may include code to copy the data sections from boot device to ram,
or any other code that needs to be run prior to running the tests.
RVMODEL_DATA_BEGIN This is instantiated inside RVTEST_SIG_BEGIN macro (which also defines the label
rvtest_sig_begin) and marks the end beginning signature region
The test-target can use this macro to create a data section.
??RVMODEL_SECTION_ END This is instantiated inside RVMODEL_SIG_END macro, (which also defines the label
rvtest_sig_end) and marks the end of the signature-region.
The test-target can reserve other model specific space, sections and global labels here.
RVMODEL_IO_INIT This initializes IO for debug output
This must be invoked if any of the other RV_MODEL_IO_* macros are used
RVMODEL_IO_ASSERT_GPR_EQ(ScrReg, Reg, Value) This outputs a debug message if Reg!=Value
ScrReg is a scratch register used by the output routine; its final value cannot be guaranteed
Can be used to help debug what tests have passed/failed
Note: this macro is currently implemented as an inlined routine. It will eventually be replaced
with an out-of-line routine with parameter values in specific registers that is called by an RVTEST_ASSERT macro that calls trampoline table code to handle register save
and inline parameter extraction before calling the RVMODEL code .
RVMODEL_IO_WRITE_STR(ScrReg, String) Output debug string, using a scratch register
ScrReg is a scratch register used by the output routine; its final value cannot be guaranteed
RVMODEL_SET_[M/S/V]SW_INT Routines to set the SW interrupt for each mode.
Currently the test forces an empty macro if undefined . Future tests may change this.
RVMODEL_CLEAR_[M/S/V][SW/TIMER/EXT]_INT. Routines to clear (SW/TMR/EXT) interrupts for each mode.
Currently the test forces an empty macro if undefined . Future tests may change this.
RVMODEL FENCEI Used in the trap handler and setup code to enforce synchronization when code is overwritten
Needed if fencei is not implemented; defaults to fencei
These will be augmented with more general interrupt test macros e.g.:
RVMODEL_ASYNCH_EVENT_ADDR(BaseReg, AddrReg)
RVMODEL_ASYNCH_EVENT_DATA( BaseReg, DataReg)
RVMODEL_ASYNCH_EVENT_CMD( BaseReg, CmdReg, Delta, Cmd, [ResultReg])

## Slide 16: Pull/Issue Status
Issue# | Date | submitter | title | status | comments
332 | 08-Apr-23 | InspireSemi | On RV64 the ecall and ebreak tests throw a load unaligned exception ... |  | 
331 | 06-Apr-23 | charmitro | Riscof coverage command treats warnings as errors |  | 
Pull#330 | -5-apr-23 | cmuellner | Add support for the Zfa ISA extension |  | 
328 | 03-Apr-23 | cmuellner | All floating-point instruction tests don't have covergroups |  | 
327 | 04-Apr-23 | cmuellner | Missing overview of supported extensions |  | 
326 | 01-Apr-23 | cmuellner | Unclear label rvtest_data |  | 
325 | 01-Apr-23 | cmuellner | Useless labels in test cases |  | 
324 | 01-Apr-23 | cmuellner | Missing documentation in TestFormatSpec.adoc |  | 
Pull#323 | 01-Apr-23 | bluewww | Fix hyperlink in README.md |  | 
322 | 23-Mar-23 | mlawson-tt | Correct values in rv64i_m/K/src/<Instruction Name>-01.S are all 0s. |  | 
Pull#321 | 15-mar-23 | cmuellner | Add support for the Zicond ISA extension |  | 
320 | 08-Mar-23 | DarrenGalpin | Linked coverage report is missing |  | 
Pull#319 | 06-Mar-23 | ptprasanna | Zfh and Zfinx Test are added |  | Changes requeated
Pull#318 | 28-Feb-23 | UmerShahidengr | Updated trap handler |  | Needs more review
317 | 21-Feb-23 | ssecatchseagate | Missing illegal instruction testcase |  | 
316 | 14-Feb-23 | ssecatchseagate | Zicsr extension is not covered with in compatibility testcases | TBD | Needs SOW for Dev Partners
315 | 13-Feb-23 | algrobman | Are Atomic instructions supported? | TBD | Needs SOW for Dev Partners
313 | 11-Feb-23 | algrobman | compilation warnings | Unknown | Solved for RV32 in latest update
307 | 16-jan-23 | ssecatchseagate | Please split large floating point tests up | Should do for all tests | Need to test or make tools to do this
306 | 09-Jan-23 | ssecatchseagate | Missing coverage in the div-01.s testcase | Test must be added | **starting process to fix
305 | 09-Jan-23 | ssecatchseagate | Utilize more regs increased test coverage not specified in coverage definition |  | Nice to have, low priority
pull#301 | 12-Dec-22 | HamazKh01 | Tests of ePMP | Under review | 
300 | 11-Dec-22 | davidharrishmc | Divide and Remainder are missing overflow corner case test | Tests must be added | **starting process to fix
293 | 04-Nov-22 | algrobman | A-extension tests | Needs resource | Basic functionality, can’t test atomicity
289 | 11-oct-22 | ssecatchseagate | No c.flw or c.fsw in compressed testcases | Tests must be added | **starting process to fix
pull#284 | 19-Sep-22 | UmerShahidengr | Tests of ePMP | Under review | See 267
272 | 25-jul-22 | Allenjbaum | Macro used in crypto scalar code are mislabelled | Macro to be rmved | **starting process to fix
258 | 18 May 22 | misterjdrg | FPU: Missing test for FS bits of MSTATUS csr |  | 
pull#226 | 17-dec-21 | liweiwei90 | add support for cbo.zero in cmo extension | Needs a fix | Should be mergeable afterwards
#203 | 24-Aug-21 | Allenjbaum | Fence test has poor coverage | Test must be added | **starting process to fix
#119 | 17-jun-20 | allenjbaum | Missing RV32i/RV64i test: Fence | Test has been written | **started process to fix w/addt’l tests

## Slide 17: JIRA Status
Issue# | Date | submitter | title | status | comments
CSC-1 | 20/Aug/20 | Ken Dockser | Come up with names for the tests suites that we are creating |  | 1st step done
CSC-2 | 20/Aug/20 | Ken Dockser | Produce concise text to explain the Architecture Tests intent and Limits | done | Will become ACT policy
CSC-3 | 20/Aug/20 | Ken Dockser | Come up with an internal goal for what we wish to accomplish with the Architectural Tests |  | This is the /test coverpoint YAML
CSC-4 | 20/Aug/20 | Ken Dockser | Develop a roadmap for all the different categories of test suites that will need to be created |  | Not written
CSC-5 | 20/Aug/20 | Ken Dockser | Develop a roadmap for releases of single-instruction Architecture Tests |  | Not written
CSC-6 | 20/Aug/20 | Ken Dockser | Develop a reference RTL test fixture that can stimulate and check the CPU under test |  | Needs more discussion

## Slide 18: Non-determinism in Architectural Tests
The RV architecture defines optional and model/µarch defined behavior. This implication: there are tests that have multiple correct answers. E.g.:
  Misaligned accesses: can be handled in HW, by "invisible" traps w/ either misaligned or illegal access causes, and do it differently for the same op accessing the same address at different times (e.g. if the 2nd half was in the TLB or not)
  Unordered Vector Reduce ops: (different results depending on ordering & cancellation)
  Tests involving concurrency will have different results depending on microarchitectural state, speculation, or timing between concurrent threads (e.g. modifying page table entry without fencing)
From the point of view of ACTs, there are 2 (& sometimes more) legal answers. The golden model only generates one. Possible mechanisms to test include:
  Modify (if necessary) & configure reference model to generate each legal result, run it with each config, & accept either result from the DUT (e.g. misalign or un-fenced PTE modification)
  Provide specific handlers for optional traps? (can’t test the trap is correct then)
  Use self-testing tests(compare with list or range of allowed outcomes from litmus tests)
  Avoid tests that can generate non-deterministic results
  Ultimately: develop new frameworks that can handle concurrency along with reference models that can generate all legal outcomes
  It is the responsibility of the TG that develops an extension to develop the strategy for testing features and extensions that can have nondeterministic results

## Slide 19: Framework Requirements
The framework must:
Use the TestFormat spec and macros described therein
  (which must work - including assertions)
Choose test cases according to equations that reference the YAML configuration
Define macro variables to be used inside tests based on the YAML configuration
Include the compliance trap handler(s), & handle its (separate) signature area(s)
Load, initialize, and run selected tests between two selected models, extract the signatures, compare results, and write out a report file
Exist in a riscv github repo, with a more than one maintainer.
Be easy to get running, e.g.:
  run under a variety of OSes with the minimum number of distro specific tools.
  Not require sudo privileges
Have the ability to measure and report coverage for test generation
  Coverage specification is a separate file
  Could be a separate app

## Slide 20: Test Acceptance Criteria
Tests merged into the ACT test_suite repo must :
conform to the current format spec (macros, labels, directory structure)
  including framework-readable configurations - i.e. which ISA extension it will be tested with (using Test_Case macro parameter equations) for each test case
use only files that are part of the defined support files in the repository, including standard trap handlers
  TBD: how to install test specific (not model specific) handlers
Be able to be loaded, initialized, run, signal completion, and have signature results extracted from memory by a/the framework
run using the SAIL model and not fail any tests
generate signature values either
  directly from an instruction result (that can be saved & compared with DUT/sim)
  by comparing an instruction result with a configuration-independent value range embedded in the test code (e.g. saving above, below, within)
  by comparing an instruction result with a configuration-independent list of values (e.g saving matches or mismatched)
    (it can be useful to also return a histogram of value indices that matched)
Store each signature value into a unique memory location in a signature region that is
  delimited by standard macros embedded in the test which can be communicated to the test framework
  pre-initialized to values that are guaranteed not to be produced by a test
have defined coverage goals in a machine readable form that can be mechanically verified
improve coverage (compared to existing tests) as measured and reported by a coverage tool (e.g. ISAC)
use only standard instructions (and fixed size per architecture macros, e.g. LI, LA are allowed)
be commented in test_case header (ideally listing coverpoint covered)
Tests that are otherwise accepted, but depend on tools or simulators that have not be upstreamed must be put into a <Ext-Name_unratified>/ directory instead of <Ext-Name>/