## Slide 1: Architectural Event Generator Proposal v0.1
Arch-Test SIG
Allen Baum, Chair
2022-01-13

## Slide 2: Rationale
To properly test the architectural handling of interrupts, tests need to be able to arbitrarily cause interrupts to be generated
  Timer interrupts can be generated by Mcode, though there can be large timing uncertainty between implementations that make this difficult to reproduce on a reference model (e.g. timer phase and granularity) unless implemented by test framework
  Software Interrupts can be generated with limited coverage or using platform specific parameters and external support with much lower timing uncertainty
  External interrupts cannot be generated without external support with low timing uncertainty
There are several extensions in progress for external interrupt: AIA, Fast Interrupts, CLINT, so test support is needed
In addition, support is needed for generated asynchronous reads and writes to test the memory model
Since this has a “work product”, this will be a non-ISA TG under the ACT SIG
The charter will include
  Implementation agnostic Hart interface Spec
  A SW model of the pseudo device that can be integrated with an RTL model
  Two example shims to integrate it as Sail and Spike external functions

## Slide 3: High Level Pseudo-Device Proposal
Develop a “trick box” artificial IO device that can generate both interrupt wires and MMIO reads and writes
Tests will write to the device to schedule
  which interrupt wires (or wires) are asserted to the DUT,
  when they are asserted or de-asserted
Tests will write to the device to schedule
  when memory transactions are made to the DUT,
  the physical address to be used,
  the type of memory transactions (e.g. read, write, other?)
  the data to be written (in case of a write)
  The data that is read (in case of a read)
  Note: this is also used to deliver message signaled interrupts

## Slide 4: Diving Deeper
The pseudo-device has a C-compatible function interface
  it is called every cycle by the DUT, and monitors the the external memory bus
  The vendor is responsible for interfacing this to their DUT at a DUT specific PA
  The inputs to the function are:
    Physical address (assume XLEN, zero extended)
    WtData (XLEN) –
      interrupt signal set/clr mask (Note: interrupts are level sensitive positive polarity only)
      MSI address
      TimingDelta, operation (wired interrupt set/clr/read/write/other
    RdData (XLEN) – primarily used for debugging
    #InstRet on this cycle (4b max, zero extended) note: the eTrace extension needs this also

## Slide 5: Diving Deeper Still
Every write to the device pushes write data onto a specific FIFO, depending write address offset
There are 3 fifos at 3 separate offsets. The DUT will ignore writes to other offsets (base device address is vendor supplied in config YAML)
  Address/Mask Fifo
  WtData Fifo
  Control Fifo: TimingDelta and Operation, IntAck?
Read to other offsets will just return internal state from the fifos for debugging.
Writing the Control Fifo arms the oldest unarmed event in the address FIFO (and the WtData Fifo, if the operation is a write)
Each cycle, the called function will decrement the InstRet counter of all entries in the TimingDelta field.
When the InstRet field value decrements to (or below) zero, the operation is issued from the operation field with the parameters from Address/Mask FIFO, and optionally the WtData macro if the operation uses it, and pops them off the top.
  Writes with TimingDelta of 0 will be performed immediately – use to Ack/clear an interrupt?
Note: fifos can be written in arbitrary order except controls must be written after the parameters it uses, so you can write multiple Masks/Addresses, multiple WtDatas, and finally multiple Controls. Controls that are written without any unarmed addresses/masks will be silently ignored.

## Slide 6: External Asynch Event Support
Strawman C interface (and hart interface)
  RVMODEL_ASYNCH_EVENTGen(Instret[3:0], wt_cmd[??], wt_addr[phys_addr_sz], wt_data[XLEN-1:0], interrupt_out[XLEN-1:0], cmd_in[??], addr_in [phys_addr_sz], data_in [XLEN-1:0])
Strawman ACT Macro Interface
  RVMODEL_ASYNCH_EVENT_ADDR(BaseReg, AddrReg)
    Assembly language would store 1 word at a platform specific mmio address
  RVMODEL_ASYNCH_EVENT_DATA(BaseReg, DataReg)
    Assembly language would store 1 word at a platform specific mmio addresses
  RVMODEL_ASYNCH_EVENT_CMD(BaseReg, CmdReg, Delta, Cmd, [ResultReg])
    Assembly language would construct and load or store 1 word at a platform specific mmio addresses
    Delta and Cmd could be a constant or a register – TBD
Notes: st

## Slide 7: Questions
How should multiple TimingDeltas simultaneously becoming <=0 be handled?
  E.g.Issue at most one wired & 1 write?
  Just one at a time in fifo order?
Should we allow events to be taken out of middle of the fifo or go strictly in order?
Which operations are needed besides Rd and Wt? (e.g.inval, snoop…)
  Is a single XLEN width write adequate?
Precisely what should the read/write interface be
  e.g. AXI subset?
  Do we need an explicit mux to interface with memory?
Control
dT Op
Addr
/Msk
Data
Wt Data
Addr Dcode
Int Wires
#InstRet
Int Wires
-
Set/Clr
Wt Addr
Wt Req
Op
Op Addr
Op Data
DUT
Mem System